## Slide 1: Amplitude Modulation Contd.

## Slide 2: DSB  SSB
Message signal
DSB signal

## Slide 3: Single sideband (SSB)
Each sideband
has enough
info to reconstruct
the message
(Move in by fc
extract I component)
Message is the I component of an SSB signal.
What is the Q component?

## Slide 4: Single Sideband Modulation
In SSB modulation, we send either the upper sideband or the lower sideband of a DSB-SC signal.
Each sideband provides enough information to reconstruct the message. But how do we physically reconstruct the message from an SSB signal?
The baseband message can be reconstructed if we can move the component near +fc to the left by fc, and the component near −fc to the right by fc; that is, if we move in the passband components towards the origin.

## Slide 5: Complex envelope for SSB signal
USB passband
USB complex envelope

## Slide 6: Complex Envelope of SSB Signal
To reconstruct the baseband message, we need to move the component near +fc to the left by fc, and the component near −fc to the right by fc. The frequency translations can be accomplished by multiplying the USB signal by 2cos(2πfct) = ej2fct + e−j2fct, which creates the desired message signal at baseband, as well as undesired frequency components at ±2fc which can be rejected by a lowpass filter.
The same argument applies to LSB signals as well. SSB signals can be demodulated in exactly the same fashion as DSB-SC, using the coherent demodulator depicted. Demodulator simply extracts the I component of the passband signal, the I component of the SSB signal must be the message.

## Slide 7: Complex Envelope of SSB Signal
The I And Q components can determined as:

## Slide 8: I and Q components for SSB
USB complex envelope
USB I and Q components

## Slide 9: I and Q components for SSB
The I component Uc(f) = M(f), and the Q component is a transformation of given by
The Q component is a filtered version of the message, where the filter transfer function is H(f) = −jsgn(f). This transformation is given a special name, the Hilbert transform the message

## Slide 10: Hilbert transform
(90 degree phase shift over all positive frequencies)

## Slide 11: I component = message Q component = message Hilbert transform

## Slide 12: Hilbert Transform
Physical interpretation of the Hilbert transform: If x(t) is real-valued, then so is its Hilbert transform ˇx(t). Thus, the Fourier transforms X(f) and ˇX (f) must both satisfy conjugate symmetry, and we only need to discuss what happens at positive frequencies.
For f > 0, we have
ˇX(f) = −jsgn(f)X(f) = −jX(f) = e−jp/2X(f). That is, the Hilbert transform simply imposes a π/2 phase lag at all (positive) frequencies, leaving the magnitude of the Fourier transform unchanged.

## Slide 13: Hilbert Transform
These transforms effectively phase shift a function by 90 degrees independent of frequency. Hilbert transforms are useful in creating signals with one sided Fourier transforms.
90 Degree Phase Shifters: We need a function that will transform a sinusoid to another sinusoid with the same amplitude and frequency but simply phase shifted by 90 degrees.
cos(q-90)=sin(q); sin(q-90)=-cos(q)
We need the transform to do the following:
cos(q) sin(q); sin(q)-cos(q)

## Slide 14: Hilbert Transform
Fourier Transform pairs:
cos(2pf0t) (d(f-f0)+d(f+f0))/2
sin(2pf0t) (d(f-f0)-d(f+f0))/2j
The transform should such that
(d(f-f0)+d(f+f0))*H(f) = (d(f-f0)-d(f+f0))/j=-j* (d(f-f0)-d(f+f0))
(d(f-f0)-d(f+f0))*H(f) = -j*(d(f-f0)+d(f+f0))

## Slide 15: Example
Based on the preceding argument, a sinusoid s(t) = cos(2πf0t+φ) has Hilbert transform ˇs(t) = cos(2πf0t+ φ− p/2 ) = sin(2πf0t+φ).

## Slide 16: Example
Based on the preceding argument, a sinusoid s(t) = cos(2πf0t+φ) has Hilbert transform ˇs(t) = cos(2πf0t+ φ− p/2 ) = sin(2πf0t+φ).

## Slide 17: I and Q components for SSB (repeat)
The I component Uc(f) = M(f), and the Q component is a transformation of given by
The Q component is a filtered version of the message, where the filter transfer function is H(f) = −jsgn(f). This transformation is given a special name, the Hilbert transform the message

## Slide 18: Time domain representation of SSB signals
From the spectrum relationship, we have
Uc(f)=M(f)
Us(f) = (-jsgn(f))M(f)
U(f)=Uc(f)+jUs(f)
Complex Envelope: u(t) = uc(t)+jus(t)
up(t)=uc(t)cos(2pfct) – us(t)son(2pfct) (USB)
What about LSB?

## Slide 19: Implementing SSB in baseband
Implementing Hilbert transform in baseband avoids need
for sharp filtering at passband

## Slide 20: SSB for sinusoidal message

## Slide 21: SSB demodulation
Synchronous demodulation to extract I component
  Vulnerable to carrier phase offset
I component
attenuation
interference
Complex envelope with respect to receiver LO
Passband received signal, phase offset wrt receiver LO

## Slide 22: SSB demodulation: non-coherent
Can add strong carrier component and employ envelope detection
Message info preserved in envelope
as long as
SSB + strong carrier component

## Slide 23: VSB Modulation
VSB is similar to SSB, in that it also tries to reduce the transmitted bandwidth relative to DSB, and the transmitted signal is a filtered version of the DSB signal. The idea is to mainly transmit one of the two sidebands, but to leave a vestige of the other sideband in order to ease the filtering requirements.
The passband filter used to shape the DSB signal in this fashion is chosen so that the I component of the transmitted signal equals the message.
2m(t) cos 2πfct ↔ M(f − fc) +M(f + fc)
This is filtered by a passband VSB filter with transfer function Hp(f), to obtain the transmitted signal with spectrum
UVSB(f) = Hp(f) (M(f − fc) +M(f + fc))

## Slide 24: VSB signaling
Filter DSB signal so as to leave vestige of one sideband
(generalizes SSB)

## Slide 25: How to choose VSB filter
I component = message
Q component = filtered version
of message that cancels
portion of spectrum

## Slide 26: Example
Problem 3.4 Consider a message signal m(t) = cos(2πfmt + φ), and a corresponding DSB-SC signal up(t) = Am(t) cos 2πfct, where fc > fm.
(a) Sketch the spectra of the corresponding LSB and USB signals (if the spectrum is complex valued, sketch the real and imaginary parts separately).
(b) Find explicit time domain expressions for the LSB and USB signals.

## Slide 27: QAM signaling
Both I and Q components carry information
Standard practice in modern digital communication systems
Will see much more of this in Chapter 4 and beyond…

## Slide 28: Carrier sync requirement for QAM
Complex envelope when there is phase offset wrt receiver LO
Effect of rotation on I and Q components
Phase offset typically estimated and corrected for
after downconversion in modern systems

## Slide 29: Example

## Slide 30: Example 3.2.4
(time in milliseconds, carrier frequency 600 KHz)
Magnitude spectrum and bandwidth of AM signal?
Message signal
AM signal

## Slide 31: Example 3.2.4 contd.
AM signal passed through an ideal highpass filter with cut-off frequency 595 KHz.
Find explicit time domain expression for Q component of output (relative to 600 KHz
reference)
Easiest to just take inverse Fourier transform of complex envelope
(see text for alternative approaches)
Q component